## Slide 1: Understanding Ozone Feed Gas Systems
<number>
The Benefits of Oxygen as the Preferred Feed Gas for Aquatic Life Support Systems
AALSO 2011

## Slide 2: Ozone Disinfection for Aquariums
<number>
  Ozone is the preferred disinfection/oxidation option
  Highly effective and is safe for living things
  Feed gas conditioning is required for all ozone generators
  There are technical options in ozone system design

## Slide 3: Oxygen vs. Dried Air Feed Gas
<number>
  Ozone generators manufacture ozone from a feed gas
  Feed gas must be “conditioned”; humidity is a major problem, causing nitric acid corrosion
  Feed gas must be dried to very low dew point
  Older technology used dried air as feed gas
  Advanced technology uses oxygen concentrators, removing water, impurities and nitrogen

## Slide 4: Oxygen Feed Gas is the Superior Choice
<number>
  Oxygen systems
    Have less components
    Require less maintenance
    Are is more efficient
    Have almost no nitrogen
  Oxygen is better for animals in aquariums

## Slide 5: Evolution of Ozone Feed Gas Technology
<number>
  1906: dried air (using desiccant) for municipal water treatment
  1940’s: Early Pressure Swing Adsorption (PSA) air driers deliver low oxygen concentration (21% oxygen) – and still do
  1958: PSA oxygen concentrators yield very dry feed gas with ~93% oxygen for efficiency

## Slide 6: Dried Air Systems
<number>
  Desiccant (replaceable system), thermal swing adsorption (TSA) (regenerate with heat); and PSA (self-regenerative) most commonly used
  Feed gas typically 21% oxygen, 78% nitrogen, 1% trace gases
  Properties of PSA air dryers:
    Input air compressed to 100 psi – 70% of the air recovered for feed gas
    Total air flow about 2 X oxygen system for same ozone output
    Continuous maintenance required
    Dew points -30F to -100F

## Slide 7: Oxygen Fed Systems
<number>
  Pressure Swing Adsorption technology
  Feed gas typically 93% oxygen, 3.1% nitrogen, 3.8% argon, 0.1% trace gases
  Properties
    Input air at 25 to 90 psi (depending on size), 9% of the air recovered as oxygen
    Highly reliable PSA oxygen concentrators sourced from healthcare
    Very low dew points typical, at -100F

## Slide 8: Oxygen System is Efficient X 2
<number>
  Oxygen fed systems more efficient than dried air when measured a variety of ways
    Oxygen fed ozone generators make at least twice the ozone (grams/hour) as same sized generator using dried air
    O2 systems produce ½ gas flow as dried air system
    O2 systems make ozone concentration 2 times greater than dried air

## Slide 9: Oxygen Systems Provide Better Performance
<number>
  Higher ozone concentration provides better mass transfer of ozone into solution
  Less off-gas, for a safer and more efficient system
  Lower total gas flow permits smaller booster pumps and smaller injectors and even smaller side-stream flow

## Slide 10: Oxygen Ozone Systems are More Reliable
<number>
  Dried air systems produce 3 to 4 times the nitric acid as oxygen systems, with more corrosion
  More maintenance is required
  Oxygen concentrator molecular sieve is highly reliable
  Molecular sieve material does not require replacement

## Slide 11: Summary: Oxygen Feed Gas is the Right Choice
<number>
  Lower investment cost in system
  Smaller footprint
  Lower operational costs
  Simplified management
  Far less equipment maintenance
  Maximum efficacy

## Slide 12: Animal Health is the Point
<number>
  System efficiency is pointless without a positive effect
  Oxygen fed system disinfects effectively
    Kills microorganisms on contact
    Rapidly oxidizes organic and inorganic matter
    No dangerous byproducts
  Are there side effects?

## Slide 13: Feed Gas Changes Water Chemistry
<number>
  Gas dissolved in water reflects composition of feed gas
  Dried air systems may increase levels of dissolved nitrogen
  Oxygen systems introduce no nitrogen
  Oxygen systems introduce only small amount of oxygen (3.2 PPM max)

## Slide 14: Dissolved Nitrogen Can Be Dangerous to Fish
<number>
  Dissolved gases threaten Gas Bubble Disease
  Nitrogen concentration from dried air system makes nitrogen narcosis the greater threat
  The likelihood of excessive nitrogen occurring in the water is greater in an air-fed system

## Slide 15: Can Higher Dissolved Oxygen(DO2) Be a Threat?
<number>
  Assuming maximum system parameters, DO2 is limited and an unlikely threat
  In this example, oxygen fed system will lead to 3.2 PPM DO2 increase based on 93% oxygen feed gas
    20C water temp assumed
    Ozone injected into 20% sidestream (or less)
    95% mass transfer rate
    15 psi contact/degas tank
  All aquariums must provide the means to control super-saturation of any dissolved gases

## Slide 16: Dissolved Oxygen in Natural Water Bodies
<number>
  Put increase from oxygen systems in perspective
  DO2 exists already in natural water bodies
    Salt water: normal 7.5 – 8.5 PPM (mg/l) at 20C; high level is 12 PPM
    Coral reefs: normal is 4 – 6 PPM (mg/l) at 20C
    Fresh water: normal 9 PPM (mg/l) at 20C; high is 10 PPM

## Slide 17: Aquarium Limits for DO2
<number>
  In aquarium, 12 PPM dissolved oxygen turns water “milky”, prompting reduction
  In aquarium, 20 PPM can begin to kill aquatic life
  Any super-saturated gases are dangerous to aquatic life

## Slide 18: Oxygen Demand
<number>
  Aquatic life needs dissolved oxygen
  Small amount of added oxygen from ozone system can be beneficial
  All aquariums have an oxygen demand
  Aquatic life can be in danger if there is not enough DO2 in the water

## Slide 19: Aquarium Water Quality
<number>
  In all cases, a properly designed commercial aquarium will provide the means to control super-saturation of any dissolved gases in the animal habitat.
  The use of oxygen-fed ozone systems offers controlled mass-transfer, manageable operation of the entire system, smaller footprint for injector assemblies, smaller de-gas system, and easier maintenance of the ozone system in general with dramatically reduced nitric acid build-up.

## Slide 20: Mass-Transfer
<number>
Henry's Law Formula
  ep = ekc
Where:
e = natural logarithm
p = partial pressure of the solute above the solution
c = concentration of the solute in the solution
k = Henry's constant
  Taking the natural logarithm of the formula, gives us the more commonly used formula:
  p = kc
The most efficient way to get the ozone into the water is to raise the O3 concentration and lower the gas to liquid ratio (volume of gas/volume of liquid [Vg/Vl ])
Raising the ozone concentration, while lowering the gas to liquid ratio, and operating under the highest pressure available with the most aggressive mixing components provides the most efficient mass transfer

## Slide 21: Basic Ozone System (without protein skimmer)
<number>

## Slide 22: Basic Ozone System (with protein skimmer)
<number>

## Slide 23: References
<number>
International Ozone Association
US Environmental Protection Agency (EPA)
Louisiana State University
Water Research Center
Fish Disease – Diagnosis and Treatment- Edward D. Nova
Steve Kaiser Vice President – Marine Science & Engineering Atlantis Resorts
Dave Derk - Lead Life Support/Water Quality Brookfield Zoo
Chart SeQual Technologies, Inc.
AirSep Corporation, Inc.
Mazzei Injector Corporation
Cloward H2O
RICE International Consulting Enterprises (Ozone Consultant)
RKS Ozone Consultants
DEL Ozone
Fin-tek Ozone

## Slide 24: Aquarium animals thrive in a clean, natural environment
<number>
  THANK YOU!
  Mickey Walsh
  Field Application Engineer
  Fin-Tek Corporation
  6 Leo Place
  Wayne, NJ 07470
  Office 973-988-1086
  Cell 862-368-4122
  mickey@fin-tek.com